## Slide 1: DDR4
POWER MANAGEMENT

## Slide 2: Self-Refresh Mode
The memory controller automatically puts the SDRAM into self-refresh after the memory controller is idle for SR_TIM number of DDR clock cycles and the LP_MODE field is set to 2h.
The LP_MODE and SR_TIM fields are programmed in the power management control register (PMCR).

## Slide 3
The memory controller completes all
pending refreshes before it puts the DRAM into self-refresh.
In self-refresh mode, the memory controller automatically stops the clocks DDR[x]_CLK[y] to the SDRAM.
The memory controller maintains DDR[x]_CKE low to maintain the self-refresh state.

## Slide 4: Power Management Control Register (PMCR)
3-0 CS_TIM : bits of PMCR
Power Management timer for Clock Stop. The DDR controller puts the external SDRAM in clock stop mode after the DDR controller is idle for these number of DDR clock cycles and if LP_MODE field is set to 1.
0 Immediately enter Clock Stop Mode
1h Enter Clock Stop Mode after 16 clocks
2h Enter Clock Stop Mode after 32 clocks
3h Enter Clock Stop Mode after 64 clocks
4h Enter Clock Stop Mode after 128 clocks
5h Enter Clock Stop Mode after 256 clocks

## Slide 5
6h Enter Clock Stop Mode after 512 clocks
7h Enter Clock Stop Mode after 1024 clocks
8h Enter Clock Stop Mode after 2048 clocks
9h Enter Clock Stop Mode after 4096 clocks
Ah Enter Clock Stop Mode after 8192 clocks
Bh Enter Clock Stop Mode after 16384 clocks
Ch Enter Clock Stop Mode after 32768 clocks
Dh Enter Clock Stop Mode after 65536 clocks
Eh Enter Clock Stop Mode after 131072 clocks
Fh Enter Clock Stop Mode after 262144 clocks

## Slide 6: 7-4 SR_TIM BITS OF PMCR
Power Management timer for Self Refresh. The DDR controller puts the external SDRAM in Self Refresh Mode after the DDR controller is idle for these number of DDR clock cycles and if LP_MODE is set to 2h.
0 Immediately enter Self Refresh Mode
1h Enter Self Refresh Mode after 16 DDR Clocks
2h Enter Self Refresh Mode after 32 DDR Clocks
3h Enter Self Refresh Mode after 64 DDR Clocks
4h Enter Self Refresh Mode after 128 DDR Clocks
5h Enter Self Refresh Mode after 256 DDR Clocks
6h Enter Self Refresh Mode after 512 DDR Clocks

## Slide 7
7h Enter Self Refresh Mode after 1024 DDR Clocks
8h Enter Self Refresh Mode after 2048 DDR Clocks
9h Enter Self Refresh Mode after 4096 DDR Clocks
Ah Enter Self Refresh Mode after 8192 DDR Clocks
Bh Enter Self Refresh Mode after 16384 DDR Clocks
Ch Enter Self Refresh Mode after 32768 DDR Clocks
Dh Enter Self Refresh Mode after 65536 DDR Clocks
Eh Enter Self Refresh Mode after 131072 DDR Clocks
Fh Enter Self Refresh Mode after 262144 DDR Clocks

## Slide 8: 10-8 LP_MODE bits of PMCR
Automatic Power Management Enable
1h Clock Stop Mode
2h Self Refresh Mode
4h Power Down Mode
0, 3h, Disable Automatic power management
5h-7h reserved

## Slide 9: 11 DP_DEN bits of PMCR
Deep Power Down Enable
0 Normal Operation
1 Overrides LP_MODE field setting

## Slide 10: 15-12 PD_TIM bits of PMCR
Power Management timer for Power Down. The DDR controller puts the external SDRAM in Power-
Down mode after the DDR controller is idle for these number of DDR clock cycles and if LP_MODE field is set to 4h.
0 Immediately enter Power down Mode
1h After 16 DDR cycles
2h After 32 DDR cycles
3h After 64 DDR cycles
4h After 128 DDR cycles
5h After 256 DDR cycles

## Slide 11
6h After 512 DDR cycles
7h After 1024 DDR cycles
8h After 2048 DDR cycles
9h After 4096 DDR cycles
Ah After 8192 DDR cycles
Bh After 16384 DDR cycles
Ch After 32768 DDR cycles
Dh After 65536 DDR cycles
Eh After 131072 DDR cycles
Fh After 262144 DDR cycles
31-16 bits of PMCR Reserved

## Slide 12: Power Down Mode
The memory controller automatically puts the SDRAM into Power-Down after the memory controller is idle for PD_TIM number of
DDR clock cycles and the LP_MODE field is set to 4h.
The LP_MODE and PD_TIM fields are
programmed in the power management control register (PMCR).

## Slide 13
If the Refresh Must Level is not reached before the entry into Power-Down, the memory controller does not pre-charge all banks before issuing the POWER-DOWN command.
This results in SDRAM entering Active Power-Down mode.
If the Refresh Must Level is reached before the entry into Power-Down, the memory controller pre-charges all banks and issues refreshes until the Refresh Release Level is reached before issuing the POWERDOWN command.

## Slide 14
This results in SDRAM entering Pre-charge Power-Down mode.
In Power-Down mode, the memory controller does not stop the clocks DDR[x]_CLK[y] to the SDRAM. The memory controller maintains DDR[x]_CKE low to maintain the Power-Down state.

## Slide 15: Save and Restore Mode
The DDR3/4 memory controller supports a save and restore mechanism to completely switch off power to the DDR3/4 memory controller. The following operation puts the DDR3/4 memory controller in off mode:
• An external master reads the following memory-mapped registers and saves their value external to the DDR3/4 memory controller:
– SDRAM configuration register (SDRCR)
– SDRAM configuration register 2 (SDRCR2)

## Slide 16
SDRAM refresh control shadow register (SDRRCSR)
– SDRAM timing 1 register (SDRTIM1)
– SDRAM timing 1 shadow register (SDRTIM1SR)
– SDRAM timing 2 register (SDRTIM2)
– SDRAM timing 2 shadow register (SDRTIM2SR)
– SDRAM timing 3 register (SDRTIM3)
– SDRAM timing 3 shadow register (SDRTIM3SR)
Power management control register (PMCR)
– Power management control shadow register (PMCSR)
– Peripheral bus burst priority register (PBBPR)
– System OCP interrupt enable set register (SOIESR)

## Slide 17
– DDR PHY control register (DDRPHYCR)
– DDR PHY control shadow register (DDRPHYCSR)
• Memory controller completes all pending transactions and drains all its FIFOs.
• Memory controller puts the SDRAM in self-refresh mode.
• Memory controller copies all shadow memory-mapped registers to its main registers. It is assumed that the shadow register always has the same value as its corresponding main register.
• Memory controller waits for all interrupts to be serviced.

## Slide 18
Memory controller acknowledges assertion of internal power down request.
• The internal module reset signal is asserted.
• The clocks and power to the memory controller can now be switched off.

## Slide 19
Memory controller acknowledges assertion of internal power down request.
The internal module reset signal is asserted.
• The clocks and power to the memory controller can now be switched off.

## Slide 20
• The memory controller exits self-refresh state.
• The system can now perform access to the external memory.